## Slide 1
A New Laboratory for MM-/Sub-MM-Wave Characterization of Cosmic Dust Analogs
Samuel Birsa1, Huy Do1, Frederick Williams1, Lunjun Liu1, Ryan Schonert1, Thushara Perera1, D.J. Fixsen2
1Illinois Wesleyan University, 2NASA/GSFC
Scientific Motivation
Mm/sub-mm ideal for observing dusty environments because A) thermal emission of dust peaks (T≈10-80K) and (B) dust is optically thin in this regime. Although realistic ISM dust grains are likely to be quite complex (as indicated by [1], for example), lab studies of simple cosmic dust analogs can help infer the composition, temperature, and mass of dust present in various environments. This information is useful for determining the past history/evolution as well as current energy sources and dynamics of dusty objects.
Since 1995, the advances in laboratory studies of cosmic dust analogs have helped explain observations such as: (1) The spectral index (β) of galactic dust emission (observed with COBE-FIRAS) deviating from 2 at low frequency (<600 GHz [2]), as an intrinsic property of amorphous dust species [3]; (2) The anti-correlation between dust temperature and low-frequency β (observed, for instance, by [4]) as an intrinsic property of Mg-rich silicates [5,6]
However, results from different lab groups on the same dust species differ by a factor of a few, perhaps due to systematics in the measurement scheme or difference in dust synthesis. Such differences must be eliminated before lab results can be used for quantitative interpretation of astronomical data. The aim of this project is to build an experimental setup dedicated to the study of cosmic analog dusts, with an emphasis on minimizing systematics by borrowing techniques from mm/sub-mm observational astronomy. We will characterize dusts synthesized locally, obtained commercially, and supplied by other groups using this setup.
FTS: Polarizing Michelson Interferometer
Novel design proposed for PIXIE mission [7]
Throughput (AΩ) = 14.7 mm2-sr
Frequency range: 60 GHz – 3 THz (2 – 100 cm-1)
Δf = 15GHz (0.5 cm-1)
Filter Wheel Assembly
Current Status
Bolometer system and filter wheel tested individually in liquid helium cryostat. Cryostat recently re-configured for pulse-tube cooler. Cryocooler, bolometer system, and filter wheel currently being tested together.
Mg-rich silicates produced in-house (IWU Chemistry) and characterized with FTIR, XRD, SEM, and EDS. At least 4 good samples available for study with new setup. Me- and Fe- rich dusts in hand from NASA (GSFC) dust production team.
Most parts of FTS already made (including wire grids). Awaiting production of mirror panels (from G-code). Will assemble FTS and test with other parts of system once mirrors are in.
References
[1] Westphal et al 2014, Science, 345, 786
[2] Reach et al 1995, ApJ, 451,188
[3] Mennella et al, 1998, ApJ, 496, 1058
[4] Planck Collaboration 2011, A&A, 535, A124
[5] Boudet et al 2005, ApJ, 633, 272
[6] Coupeaud et al 2011, A&A, 535, A124
[7] Kogut et al 2011, JCAP, 7, 25
[8] GNIRS system design notes <http://ww.noao.edu/ets/gnirs/SDN0022.htm>
Experimental Setup
Calibrated blackbody light source (50-1200K)
Fourier Transform Spectrometer (FTS)
Bolometer + horn
3-4 K Surface
Valve Heads pull on threads
Filter wheel
(holds up to 8 samples)
Light pipe + back-to-back
Winston cones
Advantages of Design
Compact: Lower cost, smaller moving mirror stroke
Systematics: Repeated re-focusing (5 times) keeps beam small; symmetric design of optical path cancels several systematic errors
Ease of assembly and optical alignment: Mirrors machined on 2 aluminum panels. Very few fixtures/mounts needed for optical components. Flat moving mirror. Principle ray lies on one plane.
CAD drawing of FTS assembly with central panel shown outside.
To Scale
2 Kevlar threads
for filter wheel
rotation
Radiation
Shields
For position
determination
Kapton mask
G10 frame for thermal
isolation and structural
support
WS2
dry lubricated bearings suitable for low temperature [8]
Thermometer (silicon diode)
Resistor array stycast to wheel acts as heater
Other side of filter wheel
Acknowledgements
This work is funded in part by NSF grant AST-1313261
Beam refocused with 5 ellipsoidal mirrors; each mirror images previous mirror to next mirror
To cryostat
Moving mirror, stroke ± 3mm
Vertical and 45° wire grid
polarizers
45° flat mirror folds beam into FTS plane
Blackbody
Source
Absorber
Dewar Case
For motion feedthrough to moving mirror
Vacuum-tight box
Al mirror panels
Folding mirrors
Light pipe (to cryostat)
Slots for wire grids
Recombined beam
Primary beam split at 45°-polarizer (dotted red and orange)
Only the paths of one polarization (in-out of diagram) followed here. Other paths are symmetric